Understanding Boot Process
BIOS, UEFI, etc.
Abhijit A. M.
abhijit.comp@coep.ac.in
All credits: “Hands on Booting” by Yogesh Babar

---
What do we already know about “boot sequence”?
- When POWERed-ON
  - The CPU’s IP (or CS+IR, etc) has manufacturer defined value
    - The Motherboard manufacturer has ensured that a code called “Basic Input Output System(BIOS)” is at this location
  - CPU starts doing fetch-decode-execute-repeat
    - So CPU is running BIOS
  - BIOS
    - code does a Power On Self Test (POST)
    - Initializes hardware by writing to control ports, etc.
    - Reads list of boot-devices, and finds the first available device

---
What do we already know about “boot sequence”?
  - BIOS (contd)
    - Reads “Sector-0” of the “Boot-device”, and loads it in RAM
      - Sector-0 is “boot-loader’ (at least that’s what we said!)
    - Jumps to it. Now boot-loader is running
  - Boot-loader
    - Loads the OS kernel (boot-loader somehow knows where kernel is!) in RAM
    - Jumps to kernel code
    - Now kernel is running
  - Kernel
    - Creates first process... and then fork-exec will create other processes

---
 Legacy boot
The world of BIOS + MBR

---
Primary and Logical Partitions
- Max 4 primary partitions
- Want more?
  - 2nd or 3rd or 4th partition can be made “extended”
  - Within extended partition create logical partitions

---
Primary and Logical Partitions

---
Primary and Logical Partitions

---
Windows XP installer

---
“Boot sector” is a misnomer here!
it’s more than a sector!

---
Bootloader code is in three parts!

---
Bootloader code is in three parts!
See C:\NTLDR (NTLDR-3 file) file on Windows XP
Try deleting this file and booting
C:\Windows\winload.exe is Windows kernel

---
Boot sequence of Win-Xp
Note: The diagram is “conceptual”. In reality, each stage loads the next stage in RAM and “jumps” (that is calls “jump” instruction) to the location of the next stage in RAM. NO jumps happen on disk!

---
More on boot region
- Vendor signature: Seagate, WD, etc.
- NULL (is 0, else disk is bad)
- MBR: reason why only 4 primary partitions!

---
More on boot region
- Fdisk signature
  - Can be “*” or something else
  - When *, called boot flag, or active/inactive flag

---
More on boot region
- Fdisk signature
  - Can be “*” or something else
  - When , called boot flag, or active/inactive flag, OS kernel is supposed to be loaded from partition with “*” flag
    - Makes sense only when you have multi-boot system
  - BIOS -> Bootstrap code (440 bytes) -> Bootloader (31 kB) of first partition -> where – partition which has “*” on it

---
Flowchart
- Run: BIOS
- Run: Partition-1, Bootloader part-1: Sector-0 , 440 bytes
- Run: Partition-1, Bootlaoder part-2: 31k
  - Checks where is the “*” mark, that is the active flag
    - If on partition-1
      - Run Partition-1, Bootlaoder part-3
    - Else
      - Run, Partition-x, Bootloader, part-0
- The Bootloader-3 part of whichever partition in the end
  - should be able to recognize the other operating systems
  - Linux recognizes all, windows recognizes only itself, for other OS: depends

---
UEFI
Unified Extended Firmware Interface

---
BIOS Limitations
- BIOS will only be able to jump to the first sector, which is 512 bytes.
- BIOS cannot generate good graphics/GUIs.
- You cannot use a mouse in the BIOS.
- The maximum partition size is 2.2 TB.
- The BIOS is dumb because it does not understand the bootloader or the OS.
- It struggles to initialize the new-generation hardware devices.

---
UEFI advantages
- UEFI can use the full CPU. Unlike the BIOS (which is stuck with 16 bits of processor), UEFI can access up to 64 bits.
- UEFI can use a full RAM module. Unlike 1 MB of address space of the BIOS, UEFI can support and use terabytes of RAM.
- Instead of 64 bytes of a tiny MBR, UEFI uses the GPT (GUID) partition table, which will provide an infinite number of partitions, and all will be primary partitions. In fact, there is no concept of primary and logical partitions.
- A maximum partition size is 8 zettabytes.
- UEFI has enterprise management tools.
  - Boot remotely
  - Browse internet
  - Change firmware remotely

---
UEFI advantages
- It’s a small OS
  - a) You will have full access to audio and video devices.
  - b) You will be able to connect to WiFi.
  - c) You will be able to use the mouse.
  - d) In terms of the GUI, UEFI will provide a rich graphics interface.
  - e) UEFI will have its own app store like we have for Android and Apple phones.
  - f) You will be able to download and use the applications from the UEFI app store, just like with Android and Apple phones. Hundreds of apps are available such as calendars, email clients, browser, games, shells, etc.
  - g) UEFI is able to run any binary that has an EFI executable format.
  - h) It boots operating systems securely with the help of the Secure Boot feature. We will discuss the Secure Boot feature in depth later in this book.
  - i) UEFI is backward compatible, meaning it will support the “BIOS way” of booting. In other words, operating systems that do not have UEFI support will also be able to boot with UEFI.